## Slide 1: Radar –Security Monitoring System
Nagavishnesh 21BRS1312
Indrasish M 21BRS1233
Rahul K 21BRS1619
BCSE420L
Sensors, Actuators
And
Signal Conditioning
Digital Assignment – 1

## Slide 2: Problem Statement
The goal of this project is to design and build a radar system that uses ultrasonic sensors and a servo motor to detect and track objects within a 180-degree field of view. The system should be able to accurately determine the distance and position of objects within this field and display this information in a user-friendly way. The servo motor should be able to rotate the sensors through 180 degrees, allowing the system to cover a wide area. The system should be cost-effective, reliable, and easy to operate, making it suitable for a range of applications, such as security, surveillance, and monitoring. The key challenges that must be addressed in this project include sensor calibration, signal processing, and motor control, as well as the design of a suitable user interface.

## Slide 3: Objectives/Motivation
Detection: The primary objective of the radar system is to accurately detect objects within a certain range. This could include detecting the presence of people, animals, or other objects.
Tracking: In addition to detecting objects, the radar system could be designed to track their movements over time. This could be useful for monitoring the movements of wildlife or tracking the progress of vehicles or other moving objects.
Range: Another objective of the radar system could be to accurately measure the distance to detected objects. This could be important for applications such as parking assistance, where it is necessary to determine how far away an object is from the vehicle.
Accuracy: The radar system could be designed with the goal of achieving a high degree of accuracy in both detection and tracking. This could involve optimizing the design of the ultrasonic sensors and servo motor, as well as using advanced signal processing techniques to filter out noise and other sources of interference.

## Slide 4: Contd…
Robustness: Another objective of the radar system could be to ensure that it is robust and reliable, even in challenging environmental conditions. This could involve designing the system to withstand extreme temperatures, moisture, and other factors that could affect its performance.
Speed: Depending on the application, the radar system may need to operate at a high speed in order to detect and track objects in real time. Achieving a high speed could be a key objective for the design of the system.
Integration: Finally, the radar system could be designed with the goal of being easily integrated into other systems or platforms. This could involve designing the system to be compatible with a wide range of software and hardware platforms, or making it easy to install and operate.

## Slide 5: Literature Survey/Related Work(minimum of 7 research articles)
S.No. | Title /Publisher | Authors | Year of Publication | Methodology | Advantage | Drawbacks
1 | Ultrasonic sensor without arduino using 555 timer. | Abhishek Singh | 2021 | 555 generates continuous trigger pulses which are given to the sensor which creates output voltage at echo pin that turns on the transistor and is proportional to distance from object. | Cheaper | More components and lower accuracy.
2 | Interfacing ultrasonic sensor with PIC | Ashwinth Raj | 2017 | PIC microcontroller is used instead of arduino | Simpler str. Less power consumption | Only for simpler systems. Lengthy code.
3 | IR obstacle sensor without arduino | Vats_prashant | 2017 | Voltage which turns on the transistor is proportional to temp. | Low cost | Low accuracy more prone to damage due to more components.

## Slide 6
4 | Motion Controlled LED Using HC-SR501 PIR Sensor and BC547 Transistor | lindevs | 2022 | When HC-SR501 PIR sensordetects motion, the voltage of output pin increases to 3.3V and current triggers BC547 transistor. It acts as a switch which opens circuit and turns ON an LED. | More compact design | Less accurate. Temp. dependency and low power dissipation of transistor
5 | Battery-less NFC Bicycle Tire Pressure Sensor Based on a Force-Sensing Resistor | Marti B Antonio L G R Villarino | 2021 | Low-cost tire pressure monitoring system (TPMS) for bicycles. The system is based on a battery-less near field communication (NFC) tag that integrates a pressure sensor. | Durable and compact. Heavily researched. | Complicated circuit.

## Slide 7
6 | AN ULTRASONIC SENSOR FOR HUMAN PRESENCE DETECTION TO ASSIST RESCUE WORK IN LARGE BUILDINGS | Robert Voute | 2018 | In this research both a preliminary ultrasound measuring device and signal processing algorithm have been designed. | The advantage of ultrasonic sound over other sensors or cameras is that its signal is able to pierce through smoke, does not require badges or other wearable devices and introduces little privacy and security risks. | Limited capabilities, Not that accurate.
7 | PGA460-Q1 in Ultrasonic Park Assist (UPA) | Brian Rodrigueg Akeem Whitehead | 2018 | Ultrasonic park assist is also known as a parking assist system, parking guidance system and reverse park assist. These systems vary from simply detecting an object’s presence and alerting the driver with a noise to autonomously parking the car with little to nodriver interaction | Researched and verified by Texas Instruments. | Ultrasonic sensor ability depends on external factors.

## Slide 8: Research Gap
Performance evaluation: There is a need to evaluate the performance of the radar system using ultrasonic technology and servo motors. This can be done by measuring the accuracy, precision, and reliability of the system in detecting and tracking targets at various distances and angles.
Noise reduction: Ultrasonic technology is susceptible to noise interference from various sources, such as wind and other environmental factors. There is a need to investigate methods to reduce noise interference and improve the signal-to-noise ratio of the system.
Control system optimization: The servo motors used to rotate the ultrasonic sensor need to be precisely controlled to ensure accurate and timely data acquisition. Research could focus on developing optimized control algorithms for the servo motors to improve the accuracy and speed of the system.
System integration: The integration of the ultrasonic sensor, servo motors, and control system is critical to the success of the radar system. Research could focus on optimizing the integration process to improve the overall performance of the system.

## Slide 9: Contd…
Power consumption: The radar system using ultrasonic technology and servo motors requires a significant amount of power. Research could focus on developing power-efficient designs and optimizing power management strategies to reduce power consumption and extend battery life.
Environmental factors: The performance of the radar system can be affected by various environmental factors, such as temperature, humidity, and atmospheric pressure. Research could focus on investigating the effects of these factors on the system and developing methods to compensate for them.
Range extension: Ultrasonic technology is limited in range compared to other radar technologies, such as microwave and millimeter-wave radar. Research could focus on developing methods to extend the range of the ultrasonic radar system without sacrificing accuracy or speed.

## Slide 10: Block Diagram/Methodology

## Slide 11
1. Gather your materials:
Arduino board
Ultrasonic sensor
Servo motor
Jumper wires
Breadboard
USB cable
Computer
2. Connect the ultrasonic sensor to the Arduino board:
Connect the sensor's VCC pin to the Arduino's 5V pin.
Connect the sensor's GND pin to the Arduino's GND pin.
Connect the sensor's TRIG pin to the Arduino's digital pin 9.
Connect the sensor's ECHO pin to the Arduino's digital pin 10.
3. Connect the servo motor to the Arduino board:
Connect the servo motor's power wire to the Arduino's 5V pin.
Connect the servo motor's ground wire to the Arduino's GND pin.
Connect the servo motor's signal wire to the Arduino's digital pin 3.
Methodology

## Slide 12
•
4. Install the Servo library on your Arduino IDE:
Open the Arduino IDE software on your computer.
Go to "Sketch" > "Include Library" > "Manage Libraries".
Search for "Servo" library and click on "Install".
5. Write the code to control the radar system:
Open a new sketch in the Arduino IDE.
Copy and paste the aappropriate code:
6. Upload the code to your Arduino board:
Connect your Arduino board to your computer using the USB cable.
Select your board type and serial port in the Arduino IDE.
Click on the "Upload" button.
7. Test your radar system:
Open the Serial Monitor in the Arduino IDE.
The servo motor should start rotating back and forth.
The ultrasonic sensor should measure the distance to an object in front of it and display it in the Serial Monitor.

## Slide 13: Why this : The Customer Question!
Accurate Detection: One of the main advantages of using a radar system with ultrasonic sensors, Arduino, and a servo motor is that it provides highly accurate detection of objects in its range.
Cost-Effective: Compared to other radar systems, a system using ultrasonic sensors and Arduino is relatively cost-effective, making it an ideal solution for various applications.
Compact Size: The use of ultrasonic sensors and Arduino makes it possible to build a compact and lightweight radar system that can be easily mounted in a variety of settings.
Easy to Install: Since the system is based on an Arduino, it is relatively easy to install and configure, even for those without a lot of technical experience.

## Slide 14
Easy to Program: The Arduino platform offers a user-friendly programming interface, which makes it easy to program the radar system to suit a variety of applications.
Low Power Consumption: The use of ultrasonic sensors and Arduino allows the system to operate on low power, which can extend the life of the system and reduce energy costs.
High Range: With the ability to rotate the ultrasonic sensor through 180 degrees using a servo motor, the system can cover a wide range, making it ideal for use in large areas.
Fast Response Time: The use of ultrasonic sensors and Arduino allows for fast response times, which is important in applications where quick detection is essential.
Flexibility: The radar system can be customized to suit a variety of applications, making it a flexible solution for a range of uses.
Real-Time Data: The system can provide real-time data on the location of objects within its range, making it useful for tracking and monitoring applications.

## Slide 15: References (Links, Books, Journals, Conference Papers)
Journals:

## Slide 16
opyright Year 2011
ttps://www.mdpi.com/2673-4591/24/1/8

## Slide 17
Thank You